## Slide 1: Solar Sails for Remote Sensing, Space Weather, and Communications
Ben Diedrich
NOAA Satellite and Information Service
NOAA Technology Summit
November 3, 2010

## Slide 2: Abstract
Solar sails are large, lightweight mirrors that push spacecraft by the gentle pressure of reflected sunlight. In the vicinity of Earth, the gentle, continuous, fuel-free thrust of solar sails enables whole new families of orbits with a new perspective on the Earth and sun-Earth connection. Solar sails may enable early detection of space weather events that disrupt power grids, communications, and navigation. They may also enable continuous monitoring of polar weather and climate parameters, and intercalibrate multiple observing systems in space and on Earth. NASA’s Galileo mission to Jupiter provided valuable remote sensing proxy data during an Earth flyby in 1990. The unique vantage point of solar sails may also enhance data transfer from polar satellites and polar ground stations. Solar sails are no longer science fiction; the Japan Aerospace Exploration Agency (JAXA) is flying the first solar sail spacecraft on a test flight to Venus. Several small Cubesat solar sail spacecraft are under development for flight over the next few years. Prior NASA research developed high performance sail technology on the ground.

## Slide 3: Summary
Solar sails & solar sailing
Why NOAA?
Orbits
Space Weather
Weather and Climate
Communications
Challenges
Opportunities

## Slide 4: Sailing
Sail deflects
“stuff”
“Stuff” with momentum
(e.g. air, sunlight)
Force on “stuff” from deflection by sail
Equal & opposite
Force on the sail

## Slide 5: Solar Pressure
Sunlight
  Electromagnetism
    Electric field induces current, magnetic field induces force
  Relativity
    Photons have momentum: E=mc2 -> p=E/c
  Low pressure: ~9x10-6 N/m2
Solar wind
  Charged particles
  Thousands of times less pressure
  Highly variable
E
B
j
jxB
B
E
j
jxB
Incident
Reflected

## Slide 6: Solar Sails
All spacecraft perturbed by solar pressure, some employ it
Large, lightweight mirror maximizes acceleration from sunlight
Numerous ground developments, orbital & suborbital deployments
Japan Aerospace Exploration Agency (JAXA) flying the first solar sail to Venus
  Interplanetary Kite-craft Accelerated by Radiation Of the Sun (IKAROS)
1993, SRC Znamya-2
20-m orbital reflector
1996, NASA/JPL/L’Garde
14-m Inflatable
Antenna Experiment
2005, Cosmos 1 flight
launch vehicle failure
1981, WSF 15-m ground demo
1999, DLR 20-m ground demo
2004, NASA/L’Garde
20-m prototype
2004, NASA/ATK
20-m prototype
GOES I-M
solar sail & trim tab
2010 JAXA IKAROS flight

## Slide 7: Solar Sailing
Steering the sail points force direction
Force from absorbed sunlight & reaction force from reflected sunlight
  Total force perpendicular to sail
Pointing with orbit velocity grows orbit, sailing away from the sun
Pointing against velocity shrinks orbit to sail towards the sun
Incident
Reflected
Total
force

## Slide 8: Why NOAA?
Space weather
Communications
Weather
Climate
Notes: Earth & human civilization

## Slide 9: Lagrange Orbits
Orbits closer to the sun than Earth move faster; those farther move slower
At L1, Earth’s gravity subtracts from the sun’s gravity (at L2 it adds), changing the orbit speed to match Earth’s
NASA Advanced Composition Explorer (ACE) and Solar and Heliospheric Observatory (SOHO) orbit L1, 1.5Mkm sunward of Earth
ACE detects solar wind changes leading to geomagnetic storms at Earth 30-60 minutes later

## Slide 10: Artificial Lagrange Orbits (ALOs)
Continuous thrust subtracting from solar gravity (adding to Earth’s) can move a Lagrange orbit closer to the sun than L1
Thrust out of the orbit plane can lift a Lagrange orbit high enough to view Earth’s poles year round
Solar sails, ion engines, combination of the two
Solar sails maintain without propellant
1.5 Mkm
150 Mkm
to sun

## Slide 11: Sail Performance & ALOs
Sail of given performance (mass/area) has choice of orbit positions
Earth
L1
L2

## Slide 12: Solar Wind
Solar wind disturbances impact Earth’s magnetosphere causing geomagnetic storms
Damaging currents in power grids & oil pipelines
Ionosphere disruption degrading communications & navigation

## Slide 13: Solar Wind Observation
Present
  NASA Advanced Composition Explorer in L1 orbit
Planned
  Deep Space Climate Observatory (DSCOVR)
Future
  Commercial service?
  Sub-L1 solar sail
    2X to 10X warning time?
Notes: Bottom line: Solar sails increase warning time.
Prior NOAA/NASA/DoD project (NOAA funded) Geostorms: 2X warning time with near-term technology
SWPC director has expressed that 10X early warning – a stretch goal for near-term sail technology – would align with the desire for L5 observations of heliospheric coronal mass ejections and solar wind streams

## Slide 14: Aurora & Ionosphere
Auroral boundary, energy deposition, and imagery are used to identify impacts to radar operations and communications in polar latitudes.
Ionospheric scintillation affects HF communications at high latitudes

## Slide 15: Auroral & Ionospheric Scintillation Observation
Present
  Maps stitched together every few hours from particle detectors and imagers on polar environmental satellites
Future?
  UV imagers in polar L2 ALOs would produce hemispheric auroral maps near realtime
  Radio beacons in polar ALOs coupled to array of ground receivers for scintillation measurement, augmented by UV imaging
Notes: Bottom line: Polar satellites provide geographic coverage but poor temporal coverage (hours between passes, stiched together into maps), but solar sails enable realtime, hemispheric view of the entire aurora from 2 satellites.

## Slide 16: Weather and Climate
Realtime, continuous, hemispheric observation of the poles
Studies over several years identified several potential applications
  Clouds
  Aerosols
  Vector winds
  Earth radiation budget
  Ozone
  Carbon gases
  Sea surface temperature
  Intersatellite calibration
  “Stitching” piecemeal high resolution LEO & GEO data
North Pole view in winter
North Pole view in summer

## Slide 17: Earth Science Proxy Data
Galileo Jupiter Mission
  Earth flyby provided similar view to Lagrange and polar ALO
Deep Space Climate Observatory (DSCOVR)
  Solar wind mission
  Imager and radiometer will observe poles for extended durations
  Higher resolution and more channels
Galileo Near Infrared
Mapping Spectrometer
Aerosols derived from Galileo
Cloud feature changes
derived from Galileo
Composite of DSCOVR
view from MODIS data

## Slide 18: Polar Satellite Communications
30 minute data latency requirement from polar environmental satellites
SafetyNet is a network of 15 ground stations under construction to handle 3 polar environmental satellites generating 15 Mbps data downlinked at 150 Mbps
Includes McMurdo, with GEO crosslink
>6 minute average, 42 minute max latency
Notes: Bottom line: Large ground network, including expensive Antarctic station with GEO crosslink, that doesn’t provide required 30 minute latency for 100% of its data.

## Slide 19: ALO Satellite Crosslink
Two solar sail spacecraft in opposite north/south ALOs
Continuous visibility of one ground station each
  ~66.5° elevation
30 seconds average, 130 seconds max latency
2 sailcraft & ground stations and near realtime data vs. 15 ground stations
Notes: Bottom line: Solar sails enable vastly reduced ground infrastructure, with 2 satellites that could serve as platforms for other requirements (SWx, remote sensing, other telecoms), with vastly improved latency.

## Slide 20: Polar Communications
National Science Foundation (NSF) operates the South Pole research station.
Limited communication coverage (several hours per day) from old geosynchronous satellites in inclined orbits.
A single ALO satellite >22.5° south of L1 or L2 has year-round visibility to the South Pole.
Remaining close to the sun-Earth line also permits solar wind monitoring.
Notes: Bottom line: Solar sails enable a single satellite to provide continuous data pipe for South Pole scientific research, that can also serve as a sub-L1 solar wind satellite.

## Slide 21: Challenges
NOAA depends on NASA for new spacecraft technologies
Current barriers to development
  NASA develops technologies for science, not operational requirements
  Changing political priorities
  Competition between technology programs
  Solar sails not flight validated despite compelling applications and progress in ground development
Research to operations transition process is long and arduous
  NASA
    Researches & develops new technology
    Flight validation
    Proposes science mission
    Flies science mission
  NOAA
    Evaluates science mission for operational utility
    Performs research to operations transition
    Flies operational mission

## Slide 22: Drivers and Opportunities
National Academy of Sciences
National Space Weather Program
NASA Space Technology Office
Small satellites (nanosatellites, cubesats)
JAXA IKAROS
DSCOVR
  Solar wind as operational NOAA capability
  Earth science research to operations opportunity
Commercial services

## Slide 23: Conclusions
Solar sails enable new orbits
Early solar wind disturbance warnings
Continuous aurora & ionosphere monitoring
Continuous hemispheric polar remote sensing
Greatly reduced infrastructure & latency for polar satellite data downlink
Continuous polar data transmission
New opportunities to overcome historical challenges