## Slide 1
Susanne Dieterle - EUMETSAT
NAEDEX-26 / ASPDEU-14 - October 2015
EUMETSAT Status Report

## Slide 2: Summary
EUMETSAT Geostationary Missions
EUMETSAT Low Earth Orbit Missions
EUMETSAT Advanced Retransmission Services (EARS)
Data Availability
Future missions

## Slide 3: Geostationary Missions
Meteosat-7, launched on 2 September 1997, has been providing the 57.5°E Indian Ocean Data Coverage (IODC) service since 5 December 2006
Meteosat-8, launched 28 August 2002, has been on station at 3.5°E since 11 February 2013.
The satellite is available as hot backup for Meteosat-10 prime service and to fill the Meteosat-9 RSS interruptions
Nominally configured in Full Earth Scan imaging mode, images archived but not disseminated

## Slide 4: Geostationary Missions
Meteosat-9, launched 21 December 2005, has been on station at 9.5°E since 5 February 2013 and supports the Rapid Scanning Service (RSS) since 9 April 2013
Meteosat-10, launched on 5 July 2012, following January 2013 relocations, has been the prime Meteosat satellite for the 0° service since 21 January 2013
The spacecraft is currently in imaging mode, fully configured including GERB-3, DCP and Search and Rescue transponders

## Slide 5: Geostationary Missions
MSG-4 was launched on 15 July 2015
After the LEOP phase by ESOC, EUMETSAT took over the responsibility for the operations of MSG-4 in orbit on 26 July
Several commissioning tests were executed with the satellite drifting and finally on 2 August 2015 the spacecraft was successfully stopped at the planned commissioning position of 3.4°W
A few dates:
  8-September – start of MSG-4 stable imaging
  22-September – start of image dissemination to selected users
  24-September – start of test product dissemination to selected users
  12-October – start of dissemination to all users in parallel with MSG-3
The MSG-4 commissioning is planned to finish in December followed by the In-Orbit Storage as of 7-December

## Slide 6: In-orbit Geostationary Spacecrafts after MSG-4 Commissioning
Met-10
3.4°W
Met-8
9.5°E
Met-9
0°
3.5°E
Rapid Scan Service
Back up
(IODC – TBD)
Prime Mission
MSG-4
In-Orbit Storage
57.5°E
IODC
Met-7

## Slide 7: Low Earth Orbit Missions – EUMETSAT Polar System
The EUMETSAT Polar System has continued to perform well and to meet its operational service specification. Metop-B and Metop-A are providing a dual-Metop operational service, with Metop-B designated as the prime Metop satellite. Metop-B half-dumps are routinely acquired over McMurdo, giving the improved data timeliness of the Antarctic Data Acquisition Service for those orbits.

## Slide 8: Status of Metop Spacecrafts
Metop-A S/C Launched 19 October 2006 | LRPT: Red | AMSU-A1: Channel 7 failed, Channel 3 NEDT is out of spec. Channel 8 NEDT is out of spec. | MHS: H3 and H4 degrading but NEDT still within spec. | AHRPT: Operated only over “secure” zones
Metop-B S/C Launched 17 September 2012 | HIRS: Channels 5, 6 and 10 currently out of spec. Others in specification. | ADCS: Degradation of received messages between 30 and 50% because of CRA antenna cable swap. as per request, run mission as ARGOS-2. ADCS transmitter is off, ADCS receiver is on. |  | SARR and SARP: Degradation of received messages in nominal beacon conditions between 0 and 10%, in worst beacon and environmental conditions up to 100%, because of CRA antenna cable swap

## Slide 9: NOAA Initial Joint Polar System Satellites
  NOAA-19, launched 6 February 2009, continues to be operated with the support of EUMETSAT as prime for ADCS and SARSAT mission services and with all other instrument data also being processed, within the IJPS framework. NOAA-19 HIRS IR Channels remain noisy
  Suomi-NPP, launched on 28 October 2011, is the first of the new generation polar orbiting satellites from NOAA in the afternoon orbit. Suomi-NPP has been the nominal IJPS satellite on the afternoon orbit since 1 May 2014.
It is recalled that EUMETSAT has no direct support to operations of Suomi-NPP. Initially a NASA satellite, EUMETSAT is however supporting global and regional Suomi-NPP data services within the scope of IJPS and in the framework of Copernicus

## Slide 10: Jason-2 - Ocean Surface Topography Mission
Jason-2, launched 20 June 2008, provides Operational Geophysical Data Record (OGDR) - which main geophysical parameters are significant wave height and ocean surface wind speed derived from the Poseidon altimeter on board the Jason2 satellite
Jason-3, follow-on of Jason-2, is due to be launched soon…

## Slide 11: Network of EARS stations and coverage
Gilmore Creek
Edmonton
Gander
Lannion
Athens
Moscow
Muscat
Saint-Dennis
Kangerlussuaq
Maspalomas
Svalbard
Wallops
Miami
Monterey
Ewa Beach
POES, Metop
Suomi NPP, POES, Metop
100 %
75-100 %
50-75 %
0-25 %
25-50 %

## Slide 12: EARS Service Status and Performance
The following services are provided by EARS:
  EARS-ATOVS, EARS-AVHRR, EARS-ASCAT, EARS-IASI, EARS-NWC
  based on Metop and NOAA data
  EARS-ATMS,EARS-CrIS and EARS-VIIRS (including DNB)
  based on Suomi-NPP data
  Overall, the availability and timeliness of these services are meeting their requirements, i.e. delivering products via EUMETCast within 10 to 30 minutes from sensing
Future: FY-3C VASS Service
  VASS – Sounder data from FY3C++ (MWTS, MWHS, IRAS)

## Slide 13: Data Availability to Users
For all EUMETSAT missions, data is available the following ways:
  In Near Real Time via:
    EUMETCast Dissemination
    GTS/RMDCN
  EUMETSAT Data Centre for archived data

## Slide 14: Future Missions – EUMETSAT Mandatory Programmes
Meteosat Third Generation (MTG)
  Imagery mission implemented by a two-satellite MTG-I system:
      Full disk imagery every 10 minutes in 16 spectral bands
      Fast imaging of European weather every 2.5 minutes
      new Lightning Imager (LI)
  Hyperspectral infrared (IRS) sounding mission:
      3D mapping of water vapour, temperature, O3 every 1 hour
      Air quality monitoring and atmospheric chemistry in synergy with GMES Sentinel-4 Ultraviolet Visible
  Full MTG mission implemented by two MTG-I satellites and MTG-S satellite in orbit
EPS-Second Generation
  Primary mission: further improvement observational inputs to Numerical Weather Prediction models
  Significant improvements of other applications, like e.g. Nowcasting at high latitudes, Marine meteorology and operational oceanography, Operational hydrology, Air quality monitoring, Climate monitoring
  Two satellites in orbit configuration:
      Metop-SG A: optical imagery and sounding mission
      Metop-SG B: microwave imaging mission
  Continuation of polar orbiting service 2021 – 2040

## Slide 15: EUMETSAT mission planning
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
YEAR...
METEOSAT FIRST GENERATION
METEOSAT SECOND GENERATION
METEOSAT THIRD GENERATION (MTG)
EUMETSAT POLAR SYSTEM (EPS)
METEOSAT-7
METEOSAT-8
METEOSAT-9
METEOSAT-10
MSG-4/METEOSAT-11*
MTG-I-1
MTG-S-1
MTG-I-2
MTG-I-3
MTG-S-2
MTG-I-4
METOP-A
METOP-B
METOP-C
EPS-SECOND GENERATION (EPS-SG)
METOP-SG SOUNDING & IMAGERY SATELLITES
METOP-SG MICROWAVE SATELLITES
JASON
JASON-2
JASON-3
JASON CONTINUITY OF SERVICES (JASON-CS)

## Slide 16: Future Missions – Sentinels for Copernicus
Most of the Sentinel missions are based on a constellation of two satellites to fulfill revisit and coverage requirements, providing robust datasets for Copernicus Services.
These missions carry a range of technologies, such as radar and multi-spectral imaging instruments for land, ocean and atmospheric monitoring. The Sentinels in which EUMETSAT is involved are:
Sentinel-3 is a multi-instrument mission to measure sea-surface topography, sea- and land-surface temperature, ocean colour and land colour with high-end accuracy and reliability. The mission will support ocean forecasting systems, as well as environmental and climate monitoring. Foreseen launch is 10 December 2015.
Sentinel-4 is a payload devoted to atmospheric monitoring that will be embarked upon a Meteosat Third Generation-Sounder (MTG-S) satellite in geostationary orbit.
Sentinel-5 is a payload that will monitor the atmosphere from polar orbit aboard a Metop Second Generation satellite.
Sentinel-6 carries a radar altimeter to measure global sea-surface height, primarily for operational oceanography and for climate studies. It is a follow-on of the Jason missions, and is implemented through the Jason-CS (Continuity of Service) space segment.

## Slide 17: Sentinel-3 Marine product contents
Level 2 OLCI:
Normalised water surface reflectance
Algal pigment concentration for open and for coastal waters
Total suspended matter concentration
Diffuse attenuation coefficient
Coloured dissolved matter absorption
Photosynthetically active radiation
Integrated water vapour
Aerosol optical depth
Aerosol Angström exponent
Level 2 SLSTR:
Sea surface temperature
(L2P GHRSST standard)
Level 2 SRAL:
Sea/coastal zone surface height
Significant wave height
Wind speed
Backscatter coefficient s0
Sea ice height, freeboard
Total water, liquid water (from MWR)
Level 1B (ESA and EUMETSAT)
- SLSTR – Sea and Land Surface Temperature Radiometer
OLCI – Ocean and Land Colour Instrument
SRAL - SAR Radar Altimeter

## Slide 18: Copernicus Sentinel-3 Payload Data Ground Segment - Overview
Online Rolling Data Archive (ODA/ORA): Supports ftp/http access to level 1&2 PDUs over the Internet
Product Dissemination Units (PDUs) apply to both EUMETCast and ODA/ORA dissemination

## Slide 19: Copernicus Sentinel-3 Payload Data Ground Segment - Elements
The Payload Data Ground Segment (PDGS) provides functions for Instrument Science Data acquisition, processing (and reprocessing), calibration, mission planning, archiving, user services and dissemination to the users
  The overall mission management being under ESA responsibility
PDGS functions (facilities) are hosted in the following Centres:
  The Marine PDGS Centre and Land PDGS Centre respectively under EUMETSAT and ESA responsibility
  The X-Band Core Ground Station(s) Centre(s) under ESA responsibility
  The Precise Orbit Determination (POD) facilities comprising:
    The Near-Real-Time (NRT) POD processing, (part of the PDGS)
    The Offline Processing centre which encompasses Short-Time-Critical (STC) and Non-Time-Critical (NTC) POD
The EUMETSAT Marine PDGS Centre includes the following facilities:
  Near Real Time (NRT) and Offline (STC, NTC) processing: L0, L1 and L2 Marine product generation, Archiving, and Dissemination, to Users
  Marine Mission Performance
  Mission Planning providing FOS/MPS with instruments operation requests
  Handling of all communications with PDGS Centres and External interfaces

## Slide 20
Thank you for your attention