## Slide 1
Nicholas Coyne - EUMETSAT
GODEX-NWP - May 2017
EUMETSAT Status Report

## Slide 2: Summary
EUMETSAT Geostationary Missions
EUMETSAT Low Earth Orbit Missions
EUMETSAT Advanced Retransmission Services (EARS)
Data Availability
Future missions

## Slide 3: Geostationary Missions
Meteosat-7, launched on 2 September 1997, has been providing the 57.5°E Indian Ocean Data Coverage (IODC) service since 5 December 2006. Meteosat-7 was turned off on 11/4/2017 at 09:00Z
Meteosat-8, launched 28 August 2002, is providing the IODC service since 1/02/2017 at a position of 41.5°E. Planned disposal mid 2020.

## Slide 4: Geostationary Missions
Meteosat-9, launched 21 December 2005, has been on station at 9.5°E since 5 February 2013 and supports the Rapid Scanning Service (RSS) since 9 April 2013
Meteosat-10, launched on 5 July 2012, following January 2013 relocations, has been the prime Meteosat satellite for the 0° service since 21 January 2013
The spacecraft is currently in imaging mode, fully configured including GERB-3, DCP and Search and Rescue transponders

## Slide 5: Geostationary Missions
MSG-4 was launched on 15 July 2015
After the LEOP phase by ESOC, EUMETSAT took over the responsibility for the operations of MSG-4 in orbit on 26 July
Several commissioning tests were executed with the satellite drifting and finally on 2 August 2015 the spacecraft was successfully stopped at the planned commissioning position of 3.4°W
The MSG-4 commissioning finished in December followed by the In-Orbit Storage as of 7-December 2015

## Slide 6: In-orbit Geostationary Spacecrafts
Met-10
3.4°W
Met-8
9.5°E
Met-9
0°
Rapid Scan Service
Prime Mission
MSG-4
In-Orbit Storage
41.5°E
IODC

## Slide 7: Low Earth Orbit Missions – EUMETSAT Polar System
The EUMETSAT Polar System has continued to perform well and to meet its operational service specification. Metop-B and Metop-A are providing a dual-Metop operational service, with Metop-B designated as the prime Metop satellite. Metop-B half-dumps are routinely acquired over McMurdo, giving the improved data timeliness of the Antarctic Data Acquisition Service for those orbits. Metop-C launch planed for October 2018.

## Slide 8: Status of Metop Spacecrafts
Metop-A S/C Launched 19 October 2006 | LRPT: Red | AMSU-A1: Channel 7 failed, Channel 3 NEDT is out of spec. Channel 8 NEDT is out of spec. | MHS: H3 and H4 degrading but NEDT still within spec. | AHRPT: Operated only over “secure” zones
Metop-B S/C Launched 17 September 2012 | HIRS: Channels 5, 6 and 10 currently out of spec. Others in specification. | AMSU-A1: Channel 15NEDT is out of spec ADCS: Degradation of received messages between 30 and 50% because of CRA antenna cable swap. as per request, run mission as ARGOS-2. ADCS transmitter is off, ADCS receiver is on. |  | SARR and SARP: Degradation of received messages in nominal beacon conditions between 0 and 10%, in worst beacon and environmental conditions up to 100%, because of CRA antenna cable swap

## Slide 9: NOAA Initial Joint Polar System Satellites
  NOAA-19, launched 6 February 2009, continues to be operated with the support of EUMETSAT as prime for ADCS and SARSAT mission services and with all other instrument data also being processed, within the IJPS framework. NOAA-19 HIRS IR Channels remain noisy
  Suomi-NPP, launched on 28 October 2011, is the first of the new generation polar orbiting satellites from NOAA in the afternoon orbit. Suomi-NPP has been the nominal IJPS satellite on the afternoon orbit since 1 May 2014.
It is recalled that EUMETSAT has no direct support to operations of Suomi-NPP. Initially a NASA satellite, EUMETSAT is however supporting global and regional Suomi-NPP data services within the scope of IJPS and in the framework of Copernicus

## Slide 10: Jason-2&3 - Ocean Surface Topography Mission
Jason-2, launched 20 June 2008, provides Operational Geophysical Data Record (OGDR) - which main geophysical parameters are significant wave height and ocean surface wind speed derived from the Poseidon altimeter on board the Jason2 satellite
Jason-3, became the reference altimetry mission on 1 October 2016 after the completion of the tandem flight phase with Jason-2 for cross-calibration purposes.

## Slide 11: Sentinel-3
Following the launch of the Sentinel-3A satellite on 16 February 2016 and the conclusion of in-orbit commissioning on 12 July, the formal handover of satellite operations from ESA took place on 13 July 2016. Most products are already operational. OLCI & SLSTR L2 are not yet operational.
RORR (Routine Operations Readiness Review) planned fro the 3/7/17. All L1 and L2 products will be operational by that date.
Sentinel-3B is planned for a Q4 2017.

## Slide 12: Network of EARS stations and coverage
Notes: Ford Island not shown

## Slide 13: EARS Service Status and Performance
The following services are provided by EARS:
  EARS-ATOVS, EARS-AVHRR, EARS-ASCAT, EARS-IASI, EARS-NWC
  based on Metop and NOAA data
  EARS-ATMS,EARS-CrIS and EARS-VIIRS (including DNB)
  based on Suomi-NPP data
  Overall, the availability and timeliness of these services are meeting their requirements, i.e. delivering products via EUMETCast within 10 to 30 minutes from sensing.
Metop-B, Metop-A, FY-3C, NOAA-19, SNPP, NOAA- 18

## Slide 14: EARS Services
SERVICE/ DB STATION | EARS ATOVS | EARS AVHRR | EARS ASCAT | EARS IASI | EARS NWC | EARS ATMS | EARS CrIS | EARS VIIRS | EARS VASS
SVALBARD | MetB N19 MetA N18 | MetB MetA N19 | MetB MetA | MetB MetA | MetB N19 | SNPP | SNPP | SNPP | FY-3C
KANGER- LUSSUAQ | MetB N19 N18 | MetB N19 | MetB | MetB | MetB N19 | SNPP | SNPP | SNPP | FY-3C
LANNION | MetB N19 MetA N18 | MetB MetA N19 | MetB MetA | MetB MetA | MetB N19 | SNPP | SNPP | SNPP | FY-3C
ATHENS | MetB N19 MetA N18 | MetB MetA N19 | MetB MetA | MetB MetA | MetB N19 | SNPP | SNPP | SNPP | FY-3C
MASPALOMAS | MetB N19 MetA N18 | MetB MetA N19 | MetB MetA | MetB MetA | MetB N19 | SNPP | SNPP | SNPP | FY-3C
MOSCOW | MetB N19 MetA N18 N15 | MetB MetA N19 | MetA MetB | MetB | MetB N19 | SNPP | SNPP |  | 
NOVOSIBIRSK | MetB N18 N19 |  |  | MetB |  |  |  |  | 
KHABAROVSK | MetB N18 N19 |  |  | MetB |  |  |  |  | 
EDMONTON | MetB N19 N18 |  |  | MetB |  |  |  |  | 
GANDER | MetB N19 MetA N18 | MetB MetA N19 | MetA MetB | MetA MetB | N19 MetB |  |  |  | 
GILMORE CREEK | MetB N19 N18 N15 |  |  |  |  |  |  |  | 
WALLOPS | MetB N19 |  |  |  |  |  |  |  | 
MONTEREY | MetB N19 MetA N18 |  |  |  |  |  |  |  | 
MIAMI | MetB N19 MetA N18 |  |  |  |  |  |  |  | 
MUSCAT | MetB N19 MetA N18 |  | MetB MetA |  |  |  |  |  | 
SAINT-DENIS | MetB N19 MetA N18 |  | MetB MetA |  |  |  |  |  | 

## Slide 15: Data Availability to Users
For all EUMETSAT missions, data is available the following ways:
  In Near Real Time via:
    EUMETCast Dissemination
    GTS/RMDCN
  EUMETSAT Data Centre for archived data

## Slide 16: Future Missions – EUMETSAT Mandatory Programmes
Meteosat Third Generation (MTG)
  Imagery mission implemented by a two-satellite MTG-I system:
      Full disk imagery every 10 minutes in 16 spectral bands
      Fast imaging of European weather every 2.5 minutes
      new Lightning Imager (LI)
  Hyperspectral infrared (IRS) sounding mission:
      3D mapping of water vapour, temperature, O3 every 1 hour
      Air quality monitoring and atmospheric chemistry in synergy with GMES Sentinel-4 Ultraviolet Visible
  Full MTG mission implemented by two MTG-I satellites and MTG-S satellite in orbit
EPS-Second Generation
  Primary mission: further improvement observational inputs to Numerical Weather Prediction models
  Significant improvements of other applications, like e.g. Nowcasting at high latitudes, Marine meteorology and operational oceanography, Operational hydrology, Air quality monitoring, Climate monitoring
  Two satellites in orbit configuration:
      Metop-SG A: optical imagery and sounding mission
      Metop-SG B: microwave imaging mission
  Continuation of polar orbiting service 2021 – 2040

## Slide 17: EUMETSAT mission planning
03
04
05
06
07
08
09
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31
32
33
34
35
36
37
38
39
40
YEAR...
METEOSAT FIRST GENERATION
METEOSAT SECOND GENERATION
METEOSAT THIRD GENERATION (MTG)
EUMETSAT POLAR SYSTEM (EPS)
METEOSAT-7 De orbited April 2017
METEOSAT-8
METEOSAT-9
METEOSAT-10
MSG-4/METEOSAT-11*
MTG-I-1
MTG-S-1
MTG-I-2
MTG-I-3
MTG-S-2
MTG-I-4
METOP-A
METOP-B
METOP-C
EPS-SECOND GENERATION (EPS-SG)
METOP-SG SOUNDING & IMAGERY SATELLITES
METOP-SG MICROWAVE SATELLITES
JASON
JASON-2
JASON-3
JASON CONTINUITY OF SERVICES (JASON-CS)
SENTINEL-3
SENTINEL-3A
SENTINEL-3B

## Slide 18
Thank you for your attention