## Slide 1: JMA Status Report
Yuki Honda
Senior Coordinator for Data Assimilation Systems
Numerical Prediction Division, Forecast Department
Japan Meteorological Agency

## Slide 2: Contents
Current Status and Recent Progress of JMA’s NWP
Status of current and future satellite system (prepared by Satellite Program Division)
Status Report of RTH Tokyo (prepared by RTH focal point for Tokyo)

## Slide 3: Current Status and Recent Progress of JMA’s NWP
Numerical Prediction Division
Forecast Department

## Slide 4: Current NWP models of NPD/JMA
 | In Operation |  |  |  | In Test Operation
 | Global Spectral Model GSM | Meso-Scale Model MSM | Local Forecast Model LFM | Global Ensemble GEPS | Meso-scale Ensemble MEPS
objectives | Short- and Medium-range forecast | Disaster reduction Aviation forecast | Aviation forecast Disaster reduction | One-week forecast Typhoon forecast | Uncertainty and probabilistic information of MSM
Forecast domain | Global | Japan and its surroundings (4080km x 3300km) | Japan and its surroundings (3160km x 2600km) | Global | Japan and its surroundings (4080km x 3300km)
Horizontal resolution | TL959(0.1875 deg) | 5km | 2km | TL479(0.375 deg) | 5km
Vertical levels / Top | 100 0.01 hPa | 48+2 21.8km | 58 20.2km | 100 0.01 hPa | 48+2 21.8km
Forecast Hours (Initial time) | 84 hours (00, 06, 18 UTC) 264 hours (12 UTC) | 39 hours (00, 03, 06, 09, 12, 15, 18, 21 UTC) | 9 hours (00-23 UTC hourly) | 264 h (00, 12 UTC) 132 h (06, 18 UTC)* 27 members | 39h 11 members
Initial Condition | Global Analysis (4D-Var) | Meso-scale Analysis (4D-Var) | Local Analysis (3D-Var) | Global Analysis with ensemble perturbations (SV, LETKF) | Meso-scale Analysis with ensemble perturbations (SV)
* when a TC of TS intensity or higher is present or expected in the RSMC Tokyo - Typhoon Center’s area of responsibility (0º–60ºN, 100ºE–180º).
Notes: This table shows specifications of the models.

## Slide 5: Assimilated Observations

## Slide 6: Status of the assimilated satellite data
[ ]: Under Development
CSR: Clear Sky Radiance on water vapor channels, AMV: Atmospheric Motion Vector
OSWV: Ocean Surface Wind Vectors, RO: Radio Occultation
Satellite/Instrument |  | GA | MA | LA
1. MW Sounder | NOAA15,18,19,Metop-A,-B,Aqua/AMSU-A | Radiation | Radiation | Radiation
 | NOAA18,19,Metop-A,-B/MHS | Radiation | Radiation | Radiation
 | DMSP-F17,18/SSMIS | Radiation | [Radiation] | [Radiation]
 | S-NPP/ATMS | Radiation | [Radiation] | [Radiation]
 | Megha-Tropiques/SAPHIR | Radiation | [Radiation] | [Radiation]
2. IR Sounder | Aqua/AIRS | Radiation | [Radiation] | [Radiation]
 | Metop-A,B/IASI | Radiation | [Radiation] | [Radiation]
 | S-NPP/CrIS | Radiation | [Radiation] | [Radiation]
3. MW Imager | DMSP-F16,17,18/SSMIS | Radiation | Radiation, Rain Rate | Radiation
 | GCOM-W/AMSR2 | Radiation | Radiation, Rain Rate | Radiation
 | GPM-core/GMI | Radiation | Radiation | Radiation
4. VIS/IR Imager | Himawari-8 | CSR, AMV | CSR, AMV | CSR, AMV
 | GOES-13,15 | CSR, AMV | - | -
 | Meteosat-8,10 | CSR, AMV | - | -
 | NOAA15,18,19,Metop-A,-B/AVHRR | AMV | - | -
 | Aqua,Terra/MODIS | AMV | - | -
 | LEOGEO composite image | AMV | - | -
5. Scatterometer | Metop-A,-B/ASCAT | OSWV | OSWV | [OSWV]
6. RO | GRACE-A,-B/Blackjack | Bending Angle | Refractivity | (Under development)
 | Metop-A,-B/GRAS | Bending Angle | Refractivity | 
 | TerraSAR-X/IGOR | Bending Angle | Refractivity | 
 | TanDEM-X/IGOR | [Bending Angle] | Refractivity | 
 | COSMIC/IGOR | Bending Angle | Refractivity | 
7. Radar | GPM/DPR | - | Reflectivity | [Reflectivity]
8. Soil Moisture | GCOM-W/AMSR2 | - | [Soil Moisture] | Soil Moisture
 | Metop-A,-B/AVHRR | - | [Soil Moisture] | Soil Moisture

## Slide 7: Updates SINCE the last meeting in 2016 GA: Global Analysis MA: Meso-scale Analysis LA: Local Analysis
Dec.2015: Metop/ASCAT Ocean Wind Vector for MA – by M. Moriya
Mar.2016: Himawari-8 AMV for GA, MA and LA – by K. Yamashita
  Dec. 2016: Revision of QC for GA
Mar. 2016: Himawari-8 CSR for GA and MA – by M. Kazumori
Mar. 2016: GPM-core/DPR for MA – by Y. Ikuta
Mar. 2016: GPM-core/GMI for GA and MA – by M. Kazumori
Mar. 2016: GNSS Radio Occultation for MA – by Y. Hirahara, H. Owada and M. Moriya

## Slide 8: ASCAT Ocean Wind Vector (M)
First guess
  Wind fields are improved in particular at lower levels.
  Similar improvements were found for other elements such as MSLP and satellite brightness temperature.
Precipitation forecast (figures are omitted):
  ETS for heavy rain (40 mm/3 hours) in the summer experiment and moderate rain (10 and 30 mm/3 hours) in the winter experiment are improved.
  The other improvements such as low level wind speed and mean sea level pressure were also confirmed.
AMV
Aircraft
RAOB
worse
better
O–B freq. distribution
ME=0.14 [m/s]
STD=1.4 [m/s]

## Slide 9: O-B normalized histograms of Himawari-8 AMVs in the Northern Hemisphere (poleward of 20N )
NH-IR-HL
NH-IR-ML
NH-IR-LL
NH-VS-LL
NH-WV-HL
0.15 2.63
-0.77 3.22
1184701
398727
H8 sample num.
MT2 sample
Num.
H8: ME STD
MT2：ME STD
1238220
254619
-0.08 2.39
-0.76 3.15
2655491
1779867
-0.16 1.65
0.03 1.73
1100327
502840
-0.09 1.56
0.02 1.60
0.44 2.65
0.31 3.28
1884951
517113
ME: Mean Error (unit m/s)
STD: Standard Deviation (unit m/s)
O-B: first guess departure
IR
(B07
+B13)
VIS
(B03)
WV
(B08
+B09
+B10)
HL：≦400 hPa
ML：400～700 hPa
LL：≧700 hPa
HL
ML
LL
O-B normalized histograms for other regions has the same characteristics.

## Slide 10: Data coverage and wind speed STD differences between TEST and CNTL on analyzed fields
●GOES-15 ●MET-7 ●LEOGEO
00 UTC 20 July 2015
CNTL
TEST
O-B wind speed STD differences (TEST-CNTL) below 700 hPa for summer 2015
Better
Worse
Normalized O-B wind speed STD differences against JMA’s wind profiler observations for summer 2015
●MTSAT
●Himawari-8
Worse
Better
Improved data coverage
Reduction of O-B wind speed differences over the Himawari-8 observation area ( especially around Japan )
Impact of revision of derived wind vector methods and introduced SPOB around Japan

## Slide 11: Results of OSE in summer 2015
Forecast lead time (hours)
Better
Worse
Normalized RMSE differences around Japan between TEST and CNTL for 850 hPa wind vectors
Average of typhoon positional errors
TEST
CNTL
BST
Typhoon track forecast of
NANGKA (T1511) initialized at 12 UTC on 13 July 2015.
Improved
Enhancement of wind speed to the northward
Enhancement of jet stream
U
V
Analyzed field of U-component and V-component winds around Japan (Zonal mean meridional cross sections: TEST-CNTL)
6% improved
Slight

## Slide 12: Himawari-8 CSR (G)
Data Usage:
Band 8 (Land, Ocean), Band 9 and 10 (only Ocean)
Averaged grid scale is changed from 64 km to 32km.
Quality Control:
Stop thinning in time, i.e. hourly data are assimilated.
Band 13 is used to detect the area of low clouds.
  B08:≥55%, B09:≥60%, B10:≥65%
Impacts on Analysis and Forecasts
Humidity fields in troposphere are improved.
Forecasts fields of T, U, Q over Japan are improved against RAOB and analysis.
Himawari8 Band 8
MTSAT-2 IR3
Assimilated CSR data numbers
Normalized changes in the STDV of OmB
(against Baseline (no Himawari8 nor MTSAT-2))
Data Num.
Red: Himawari8
Green: MTSAT-2
100hPa
1000hPa
500hPa
T
U
Q
RMSE TEST-CTRL against RAOB over Japan

## Slide 13: GPM/DPR (M)
The same 1D+4DVar method for ground-based radar data assimilation is used.
  Both KuPR and KaPR are used.
  Liquid phase data are only used.
CONTROL w/o DPR
TEST with DPR
Lead time: 33-hour Initial time: 2015-09-08 00UTC
OBSERVATION
7 Sep. 2015, 15UTC
8 Sep. 2015, 00UTC
JMA is the first NWP center to use space-borne radar data operationally.
Path of GPM-core and simulated KuPR

## Slide 14: GPM/GMI(M)
GMI is the successor of TMI.
In the pre-operation test for July 2014, GMI assimilation were compared to the TMI assimilation and baseline (w/o GMI,TMI)
While GMI assimilation showed positive impact on precipitation forecast in its OSE with JMA’s Meso Scale Model, TMI assimilation showed the better impact.
Because of the observation frequency difference, It was inferred “The more frequent observation provides the better forecast”
TMI | GMI
10.65V | 10.65V
10.65H | 10.65H
19.35V | 18.7V
19.35H | 18.7H
21.3V | 23.8V
37V | 36.64V
37H | 36.64H
85.5V | 89V
85.5H | 89H
 | 166V
 | 166H
 | 183+3V
 | 183+7V
Central frequency [GHz]
Red:
for assimilation
Thread Score 1mm/hr
Forecast hour
GMI ---
TMI ---
Baseline ---
Used data counts
GMI
TMI

## Slide 15: GNSS Radio Occultation (M)
03UTC
15UTC
Metop-A
COSMIC
GRACE-B
TerraSAR-X
Metop-B
TanDEM-X
Data Coverage on 9 Sep. 2015
NO RO
BANGLE
REFRAC
ME
RMSE
(hPa)
(hPa)
Better
NO RO
BANGLE
REFRAC
200
1000
400
600
800
200
1000
400
600
800
-0.4
-0.2
0
0.2
0.4
0.6
0.8
(K)
0.9
1.0
1.1
1.2
(K)
Improvement by using refractivity is slightly better than using bending angle.
This result suggests that the upper layer information of the model is insufficient for the assimilation of bending angle due to the limited model-top height (22km).
Results: Analysis fitting to observations
Period: 1 Jul, 2014 - 24 Aug, 2014
Statics of temperature in compared with Radio-sonde observation

## Slide 16: Updates SINCE the last meeting in 2017 GA: Global Analysis MA: Meso-scale Analysis LA: Local Analysis
Jan. 2017: Satellite Radiance Data for LA – by Y. Ikuta
  NOAA,Metop/AMSU-A; NOAA, Metop/MHS; Aqua/AMSU-A; GCOM-W/AMSR2; DMSP/SSMIS; GPM-core/GMI; Himawari-8/AHI
Jan. 2017: Satellite Soil Moisture Data for LA – by Y. Ikuta
  GCOM-W/AMSR2, Metop/ASCAT
Mar. 2017: Suomi-NPP/ATMS for GA – Y. Hirahara, T. Egawa and M. Kazumori
Mar. 2017: Suomi-NPP/CrIS for GA – M. Kamekawa and M. Kazumori
Mar. 2017: DMSP-F17,18/SSMIS(183GHz) for GA – Y. Murakami and M. Kazumori

## Slide 17: Sat. Rad. Data (L)
Assimilated satellite radiance data
NOAA,Metop/AMSU-A; NOAA, Metop/MHS; Aqua/AMSU-A; GCOM-W/AMSR2; DMSP/SSMIS; GPM-core/GMI; Himawari-8/AHI
Introduction of Variational Bias Correction (VarBC)
Predictor: Const, Scan angle, SST
17
RH: ME RMSE
ETS
T: ME RMSE
WINTER
SUMMER

## Slide 18: Soil Moisture Products of GCOM-W/AMSR2, Metop/ASCAT (L)
Asuca-Var: DA for Local Anlysis
  Analysis variables:
Observation Operator: CDF matching
Quality Control
  Elimination of the Data in Precipitation Area, Accumulated Snow Area, Forest Area, Artificial Construction Area, Water Surface Area (Ocean, Lake, River etc.)
  Gross error check
  Bias correction – predictor (predictor: const)
Impacts on Analysis and Forecasts
  Improvement of ETS around 10mm/h in Summer
  Improvement of ETS for 15mm/h in Winter
  RMSE of surface temperature is improved during daytime
  Negative bias of humidity near surface is exaggerated.
ground and skin temperature
soil volumetric water content
AMSR2
ASCAT

## Slide 19: Suomi-NPP/ATMS (G)
Data Usage:
- Only tropospheric CHs (6–9, 18–22)
- Thinning distance is 250km, independently from AMSU-A and MHS.
Quality Control of ATMS data:
- Noise filter is applied at decoding.
- QC is same to that for AMSU-A and MHS
Impact on Analysis
- ATMS assimilation improves water vapor and temperature fields in FG fields.
Impact on Forecasts
- ATMS assimilation improved forecast in mid- and upper-troposphere, especially in the Southern Hemisphere.
- It also brought slight improvement of tropical cyclone track predictions.
AAP FFT-based Noise Filtering (CH8 OmB)
OFF
ON
19
Zonal mean of RMSE(CTRL) – RMSE(TEST) of geopotential height in August 2015
FT=24
FT=48
FT=72
GMI
AMSR2
SSMIS
GNSS-RO
RAOB-T
Normalized changes in the STDV of OmB in Summer

## Slide 20: Suomi-NPP/CrIS (G)
Obs error of CrIS is smaller than that of IASI and AIRSl
CrIS assimilation improved the fitting of FG to other obs. such as AMSU-A and GNSS-RO.
It also improved geopotential height forecast in Southern Hemisphere.
MW Sounder
GNSS-RO
Usage: CHs (around 15µm) sensitive
to T --- (land) 25CH, (Ocean) 27CH
Statics period
2015.6-8 summer
2015.12-2016.02 winter
CrIS
IASI
AIRS
Wave Number(cm-1)
Obs error (K)
Observation Error of HSS
RMSE is against own analysis

## Slide 21: DMSP/SSMIS(183GHz)(G)
Data Usage: (SSMIS Imager CHs are already used.)
Clear-sky data of SSMIS 3CHs (CH 9,10, 11) around 183GHz of DMSP-F17,18
Quality Control of SSMIS(183GHz) data:
Cloud detection algorithm w/o 157GHz CH
  QCs for MHS uses 157GHz CH to identify cloudy area.
  Clouds classified into Cloud Liquid Particle, Snow Crystal and Ice Crystal are removed.
  Impacts on Analysis and Forecasts
Improved fits in FG departure of water vapor field. Mean analysis field is almost unchanged.
Positive impact for the prediction of Z and T at Southern Hemisphere.
Normalized changes in the STDV of OmB
Summer
Winter
FT=96
FT=48
FT=72
Ratio (CNTL-TEST)/CNTL
OmB of DMSP-F17/CH9
Before QCs
After QCs

## Slide 22
Japan Meteorological Agency
GODEX-NWP first Session
16-19 May 2017
JMA report on the status of current and future satellite system

## Slide 23
Satellite | Observation period
GMS | 1978 – 1981
GMS-2 | 1981 – 1984
GMS-3 | 1984 – 1989
GMS-4 | 1989 – 1995
GMS-5 | 1995 – 2003
GOES-9 | 2003 – 2005
MTSAT-1R | 2005 – 2010
MTSAT-2 | 2010 – 2015
Himawari-8 | 2015 – 2022
Himawari-9 | 2022 – 2029
GMS (Geostationary Meteorological Satellite)
MTSAT (Multi-functional Transport SATellite )
Back-up operation of
GMS-5 with GOES-9 by
NOAA/NESDIS
from May 22, 2003
to June 28, 2005
(GOES-9)
Aug 1981
GMS-2
(Himawari-2)
Aug 1984
GMS-3
(Himawari-3)
Sep 1989
GMS-4
(Himawari-4)
Mar 1995
GMS-5
(Himawari-5)
Launched in
Feb 2005
MTSAT-1R
(Himawari-6)
Feb 2006
MTSAT-2
(Himawari-7)
Launched in
Jul 1977
GMS
(Himawari)
Himawari
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸNASDA
ⒸSS/L
ⒸMELCO
Oct 2014
Himawari-8
2016
Himawari-9
Overview – Planning of JMA satellite systems
(Himawari-series)

## Slide 24
Himawari-8/9 Mission Schedule
Himawari-8 has stably been operational since July 2015.
Himawari-9, which was launched in November 2016, has started in-orbit standby since 10 March 2017.
  MTSAT-2’s meteorological mission terminated.
Himawari-9 will continue in-orbit standby until FY 2022, then will be operational until FY 2029 as a successor to Himawari-8.
Japanese
Fiscal Year

## Slide 25
02:40 UTC on 24 January 2017
First Image by Himawari-9

## Slide 26
Himawari-8/9 Satellite
H-IIA31
(Photo: Mitsubishi Heavy Industries Group)
Himawari-9
(Photo: Mitsubishi Electric Corporation)

## Slide 27
Advanced Himawari Imager (AHI)
on Himawari-8/9 Satellite
AHI : new generation GEO imager
3 VIS, 3 NIR and 10 IR bands
Full disk observing cycle: 10 min., rapid scanning within 2.5 min. / 30 sec. intervals
* Nominal value
*

## Slide 28
Mission Overview

## Slide 29
Himawari-8/9
raw data
JMA
Communication Satellite (CS)
HRIT files,
LRIT files,
SATAID files
HSD files,
NefCDF files,
PNG files
HimawariCloud service
HimawariCast
service
Users
CS Operator
C-band antenna
LNB
DVB-S2 receiver
PC & software
NMHSs
Himawari-8/9 Data Dissemination

## Slide 30
HimawariCloud service started distributing Himawari-8 in-orbit-test imagery in April 2015.
Full-disk imagery is available within 8 minutes on the HimawariCloud server.
In November 2015, HRIT data distribution started(same as the ones disseminated via HimawariCast).
Upon receiving application forms, JMA is providing HimawariCloud 23 (as of Jan. 2017) accounts for NMHSs in the East Asia and Western Pacific regions.
Observation type | Format | Notes
Full disk (10-minute intervals) | Himawari Standard Data (HSD) PNG | HSD: 16 bands (full resolution) PNG: True-color composite (1 km) HRIT files (HSD)
Target area (2.5-minute intervals) | HSD NetCDF PNG | HSD: 16 bands (full resolution) NetCDF: 16 bands (latitude/longitude grid) PNG: True-color composite (1 km)
HimawariCloud service

## Slide 31
HimawariCast service started disseminating Himawari-8 imagery in July 2015.
Communication satellite: JCSAT-2A (154 degrees East)
was followed by JCSAT-2B in
July 2016
Data type | Format | Notes
Himawari imagery (full disk) | HRIT files LRIT files Compatible with the MTSAT HRIT/LRIT services | Interval: 10 minutes HRIT: 14 bands (VIS: 1 km, IR: 4 km) LRIT: 4 bands (VIS, IR1, IR3, IR4: 5 km)
NWP products In-situ observations ASCAT ocean surface wind | SATAID format | Superimposed onto satellite imagery by SATAID software
HimawariCast service

## Slide 32
Himawari-8 and -9 have:
  a very close orbital position;
    separated by only 0.1 deg. around 140.7 degE.
  very similar spectral response.
    equipped with the Advanced Himawari Imager (AHI)
JMA ensures consistent and contiguous observation over 14 years by those two satellites.
AHI-8 and AHI-9 spectral response for VIS, NIR and IR spectral regions
Himawari-8/9 Mission Consistency

## Slide 33
In case of Himawari-8’s anomaly, back-up observation by Himawari-9 is performed.
Himawari-9’s data dissemination via HimawariCloud/Cast quickly starts after the anomaly;
  Band01-03 (VIS) : 4 hours after
  Band04-16(NIR/IR): 24 hours after
Basically, Himawari-8’s observation is also cancelled due to a scheduled satellite maintenance for several hours once a year.
In such a case, Himawari-9’s data are disseminated.
Contingency Plan

## Slide 34
Band13(10.4um), 2 February 2017
Himawari-8
Himawari-9
Consistency of Himawari-8 and -9

## Slide 35: Status Report of RTH Tokyo
RTH focal point for Tokyo
Presented by Yuki HONDA
(Numerical Prediction Division of JMA)
First Meeting on Global Operational Data Exchange
for NWP (GODEX-NWP)
(Lannion, France; 16 to 19 May 2017)

## Slide 36: GTS Connections (Apr. 2017)
December
2015
Khabarovsk
Seoul
Bangkok
Hong Kong
Manila
New Delhi
Beijing
Melbourne
Washington
2Mbps
Tokyo
64kbps
2Mbps
Exeter
10Mbps X 2
Offenbach
MPLS network
(NTT)
RMDCN
WIS Core-net. (Interoute)
Toulouse
April 2017
Doha
50Mbps
4Mbps
50Mbps
50Mbps
20Mbps
16Mbps
4Mbps
4Mbps
64Kbps
1Mbps
128Kbps
Migrated from leased line to WIS core-network
Bandwidth:
128Kbps to 4Mbps

## Slide 37: Daily Volume (WIS core-network)
GISC Tokyo connects to GISCs over the WIS core-network(RMDCN)
  Washington
  Melbourne
  Exeter
  Beijing
  Seoul
  New Delhi
  Toulouse
  Offenbach

## Slide 38: Daily Volume (NTT MPLS network)
GISC Tokyo connects to SE-ASIA counties over the NTT MPLS network
  Hong Kong
  Bangkok
  Manila

## Slide 39: Satellite Data Exchange (1) APSDEU14 to GODEX-NWP1
Metop-B/ATOVS (received at Syowa Station, Antarctica)
3 August 2016
    To Beijing, Exeter, Hong Kong, Melbourne, New Delhi, Seoul, Washington, Toulouse, Offenbach and Doha
  EUMETSAT SEVRI radiance data
  7 September 2016:
    To New Delhi
  COSMIC data
  16 November 2016
  To Hong Kong

## Slide 40: Satellite Data Exchange (2) APSDEU14 to GODEX-NWP1
Meteosat-8 (AMV, CSR, ASR, etc.)
November 2016
Indian Ocean Data Coverage (IODC) Meteosat-8 data from Offenbach
To Seoul
Metop-A,B/IASI (received at Jincheon Station)
February 2017
Metop IASI data from Seoul
To Beijing, Exeter, Hong Kong, Melbourne, New Delhi, Washington, Toulouse, Offenbach and Doha

## Slide 41: AP-RARS connectivity 2017
Asia-pacific regional RARS center
Melbourne
Tokyo
Hong Kong
Jincheon
Beijing
Guangzhou
Urumuqi
Kiyose
Syowa
Singapore
Kelburn
Maupuia
Fiji
Exeter
Washington
Crib Point1
Darwin
Perth
Townsville
Casey
Davis
New Delhi
Chennai
Guwahati
Papeete
Toulouse

## Slide 42: Thank you for your attention

## Slide 43
Thank you

## Slide 44: Thank you