## Slide 1: Update on DBNet
Nigel Atkinson
GODEX-NWP, 27-30 November 2018

## Slide 2: Introduction
From WMO web page: The Direct Broadcast Network (DBNet) is a set of operational arrangements for the real-time acquisition of Low Earth Orbit (LEO) satellite data through a worldwide network of local, Direct Broadcast receiving stations and the rapid delivery of these data to the global user community after pre-processing and formatting in accordance with agreed standards.
See the Guide to DBNet: https://wis.wmo.int/DBNet-Guide

## Slide 3: DBNet system concept

## Slide 4: Main networks
Network | Coordinators | Services | Approx number of stations
EARS | EUMETSAT | ATOVS, IASI, AVHRR, ATMS, CrIS, VIIRS, MWHS-2, IRAS, ASCAT | 16
NOAA | SSEC/UW/CIMSS | IASI, ATMS, CrIS | 13
Asia-Pacific | JMA and BoM | ATOVS, (IASI, ATMS, CrIS) | 13
South America | INPE and CONAE | ATOVS, (IASI, ATMS, CrIS) | 4

## Slide 5: Station locations
Map courtesy of JMA
A few recently-added stations are not shown

## Slide 6: What’s new since last GODEX-NWP?
Expansion of the NOAA network (ATMS, CrIS, IASI)

## Slide 7
Plus Easter Island and Pretoria
– they send raw data to SSEC for processing and onward dissemination

## Slide 8: What’s new since last GODEX-NWP?
Expansion of the NOAA network (ATMS, CrIS, IASI)
More stations are contributing ATMS and CrIS
  Tahiti, Cuiaba (Brazil), Cachoeira Paulista (Brazil), Jincheon (Korea)

## Slide 9: What’s new since last GODEX-NWP?
Expansion of the NOAA network (ATMS, CrIS, IASI)
More stations are contributing ATMS and CrIS
  Tahiti, Cuiaba (Brazil), Cachoeira Paulista (Brazil), Jincheon (Korea)
New satellites launches: NOAA20, Metop-C, FY-3D
  NOAA-20 received at most of the NOAA and EUMETSAT stations
    CrIS disseminated in FSR format (431 channels)
  Awaiting processing software from CMA for FY-3D
    MWTS-2 and MWHS-2 can be established as DBNet services
    Consider HIRAS when NWP centres have evaluated the data. BUFR sequences needs to be defined
    Consider adding MWRI as part of DBNet
  AAPP v8.3 has the Metop-C instrument calibration files

## Slide 10: NWP SAF monitoring: new-look web pages
Table is the main user interface
Click on a pass to plot it
Select specific stations, satellites or passes that generated warnings
New columns
Can sort by column headings

## Slide 11: Satellite priorities for DBNet
Trade-off between many factors, including:
  Availability of local processors
  Instrument health
  Coverage and quality of direct broadcast
  Impact on NWP (depends on many factors – including orbits, see next slide)
  Timeliness of the global data
  Local station needs (e.g. for imagery)
How does a DB station handle satellite conflicts? (i.e. where 2 or more satellites compete for the same antenna)

## Slide 12: Equator crossing times
Metop-A/B
NOAA-18
NOAA-15
NOAA-20 and S-NPP
NOAA-19
FY-3B
FY-3C
Terra
Aqua
Since last GODEX-NWP…
NOAA-15 dropped – downlink quality very poor
NOAA-19 moving towards well-separated late afternoon position
NOAA-18 is now only ~1 hour before the Metops
Launch of NOAA-20 – same orbit as S-NPP (different phasing)
Metop-A starting to drift, as orbital manoeuvres have ended
Well-separated orbits are preferable, but NWP studies have shown benefits even when 2 instruments are in a similar orbit.

## Slide 13: Timeliness of the global data (from
Times quoted are for 90% of total data, over 1 month, by DWD
AMSU, ATMS, MWHS-2
Plots taken from NWPSAF web site
M-B: 0h 50m
M-A: 1h 33m
N19: 2h 03m
NPP: 1h 48m
N18: 3h 48m
FY3C: 5h 8m
N20: 0h 50m

## Slide 15: Some current DBNet issues
FY-3C currently only received in EARS network. Encouraging other networks to participate.
Need processing software from CMA for FY-3D
CMA have defined new BUFR sequences for MWHS-2, MWTS-2 and IRAS (3-10-070, 71, 72 respectively). Already in use for global data on GTS. Need to adopt for DBNet also.
User requirement for MWRI data as part of DBNet? Technically, it should be easy to add, if a station is already processing MWHS-2.
No new BUFR sequence yet for MWRI. This will be needed.
Left-hand circular polarisation for FY-3E (some reception stations will not be able to receive it)
Migration from CrIS NSR to FSR for Suomi-NPP – time scales? Spring 2019?

## Slide 16: Questions and discussion?