## Slide 1: Update and Future of the EC/NOAA Freezing Spray Inter-Comparison
by
Serge Desjardins
LT Joseph T. Phillips *
National Lab for Marine and Coastal Meteorology (aka MAC Lab)
Halifax, Nova Scotia
National Weather Service - Ocean Prediction Center
EC/NOAA Marine Collaboration Workshop
02-05 May 2016
Ann Harbour, Michigan

## Slide 2: Contents
Return from last workshop
    Let the Equations Talk
    POAC’15 Eirik Samuelsen report
    Our algorithms have problems ? How do we fix them ?
A few observations
    Analysis
What is NEXT ? Proposing a new approach
    Probabilistic products
DiSCUSSION (Where do we go from here ?)
    Overland, Stallabrass, Sawada
    Collaboration for next year

## Slide 3
SAWADA : ƒ(Wind Speed, Temperature)
OVERLAND : ƒ(Wind Speed, Temperature, Salinity, Sea Surface Temperature)
STALLABRASS : ƒ(Wind Speed, Temperature, Salinity, Sea Surface Temperature, Wave, RH)
SAWADA
Wind Speed
Temperature
Category
Light
Moderate
Severe
Extreme
“Cloud of Possibilities”
The Freezing Spray Algorithms

## Slide 4
Slightly Deeper understanding of the equations
The thermodynamic involves
Structure
Ice
Film of water
Ta,RH
SEA : SST
Air
Td
Ts
Runoff
= ) f(n) + ) + )
Rate of icing building on an ideal cylinder
Model calibration correlating
the theoretical rate of icing on the cylinder to observational data
From reading : Norm L. Henry report,
95-004A, Newfoundland , October 1995
Droplet time
of flight

## Slide 5: Slightly Deeper understanding of the equations
Ri : rate of ice buildup per unit area : Icing Rate
Rw : rate of generation/delivery spray per unit area : Spray Flux
n : fraction of the total incident water that freezes : Frozen Spray
Challenges
In Rw : what does cause the spray ?
Parametrisation (Wind, Wave and Ship Vessel movement)
How high does the spray go (vessel size and shape) ?
In n : what does not freeze ?
Runoff water
thermodynamic processes associated with ice formation (parametrisation)
In Ri : what type of ship vessel (how high is the deck ?)
From reading : Norm L. Henry report,
95-004A, Newfoundland , October 1995

## Slide 6
= ) f(n) + ) + )
Slightly Deeper understanding of the equations
Overland
= ) f(n) + ) + )

= ) f(n) + ) + )
STALLABRASS
Evaporative cooling
Droplet cooling
Runoff
Spray cloud residence time
?
Runoff

## Slide 7: ALGORITHM’s problems from POAC’15 : Eirik Samuelsen
OVERLAND
… whenever the convective heat flux is positive (Tf-Ta),
freezing will occur and the spray flux will be 18 to 23 larger than ice accretion…
… there is always a sufficient amount of water available
regardless of the sea state and the speed vessel
…the spray flux is assumed to increase
when the air temperature decreases…unphysical

## Slide 8: ALGORITHM’s problems from POAC’15 : Eirik Samuelsen
STALLABRASS
… uses a droplet cooling time equal to the time it takes for the spray cloud
in total to pass vessels (spray cloud residence time)
… this lead to a very low droplet temperature
…probably too low, too much icing when compared
to the observations on the coast guard.
Since the droplet temperature is more comparable
to the temperature of the air
…makes the overall algorithm very little sensitive to SST.

## Slide 9: ALGORITHM’s problems
SAWADA
Used by Canadian Eastern Forecasters
NO SST dependency
 |  | Wind Speed (kt) |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
Air Temperature ( °C) | -5 | NIL | NIL | NIL | TRC | LGT | MDT | MDT | MDT | MDT | SVR | SVR | SVR | XTM
 | -10 | NIL | NIL | LGT | MDT | MDT | SVR | SVR | SVR | SVR | XTM | XTM | XTM | XTM
 | -15 | NIL | NIL | LGT | SVR | SVR | SVR | SVR | XTM | XTM | XTM | XTM | XTM | XTM
 | -20 | NIL | NIL | LGT | SVR | SVR | SVR | XTM | XTM | XTM | XTM | XTM | XTM | XTM
 | -25 | NIL | NIL | LGT | SVR | SVR | XTM | XTM | XTM | XTM | XTM | XTM | XTM | XTM
But …. SO SIMPLE to DEFINE environment for freezing spray

## Slide 10: ALGORITHM’s problems HOW do we fix them ?
Overland : No real fix.
Constant freezing fraction
Stallabrass : Smaller droplet cooling time.
Average time for droplet cooling time
Chart: 
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60
O_Stall | 7.7714 | 3.8857 | 2.5905 | 1.9428 | 1.5543 | 1.2952 | 1.1102 | 0.97142 | 0.86348 | 0.77714 | 0.70649 | 0.64761
M_Stall | 10.6066 | 9.9632 | 9.3198 | 8.6764 | 8.0331 | 7.3897 | 6.7463 | 6.1029 | 5.4595 | 4.8161 | 4.1727 | 3.5293
N2_Stall | 10.6066 | 7.6603 | 4.2681 | 2.8865 | 2.1582 | 1.7146 | 1.4183 | 1.2073 | 1.0499 | 0.92812 | 0.83127 | 0.75246
N4_Stall | 10.6066 | 9.9632 | 5.9457 | 3.8302 | 2.7622 | 2.134 | 1.7265 | 1.4432 | 1.2363 | 1.0791 | 0.95605 | 0.85731
N6_Stall | 10.6066 | 9.9632 | 7.6233 | 4.7738 | 3.3661 | 2.5534 | 2.0346 | 1.6792 | 1.4227 | 1.2301 | 1.0808 | 0.96217
N8_Stall | 10.6066 | 9.9632 | 9.3009 | 5.7175 | 3.97 | 2.9728 | 2.3427 | 1.9151 | 1.6091 | 1.3811 | 1.2056 | 1.067
N10_Stall | 10.6066 | 9.9632 | 9.3198 | 6.6611 | 4.574 | 3.3922 | 2.6509 | 2.151 | 1.7955 | 1.5321 | 1.3304 | 1.1719
N12_Stall | 10.6066 | 9.9632 | 9.3198 | 7.6048 | 5.1779 | 3.8116 | 2.959 | 2.3869 | 1.9819 | 1.683 | 1.4552 | 1.2767
N16_Stall | 10.6066 | 9.9632 | 9.3198 | 8.6764 | 6.3858 | 4.6504 | 3.5753 | 2.8587 | 2.3547 | 1.985 | 1.7047 | 1.4864
O&M | 9.189 | 6.9245 | 5.9551 | 5.3096 | 4.7937 | 4.3424 | 3.9282 | 3.5372 | 3.1615 | 2.7966 | 2.4396 | 2.0885
=
=

## Slide 11: A few observations (Analysis)

## Slide 13: Jan 13, 2016
2016-01-13 13:27 | 2016-01-13 | 10:00:00 AM | GMT -4: Atlantic Standard Time | 47 03N | 058 08W | -1C | BF 9 & BF 10 | Easterly |  | Slight icing on deck and accommodation including bridge front. | Easterly x 5 Meters |  | 

## Slide 14
OVERLAND
STALLABRASS
SAWADA
X

## Slide 15: Feb 12, 2016
12-Feb-16 |  |  | 42.635 | -69.58333 |  |  |  |  | Weather: Freezing spray, 1/8 inch per hour; Wind blowing about 45 knots
TIME UNKNOWN

## Slide 16
00 FEB 12, 2016
06 FEB 12, 2016
12 FEB 12, 2016

## Slide 17
OVERLAND
STALLABRASS
SAWADA
X

## Slide 18: Jan 05, 2016
TIME UNKNOWN
05-Jan-16 |  |  | 43.67333 | -67.685 |  |  |  |  | Weather: Freezing spray
05-Jan-16 |  |  | 43.79833 | -67.75 |  |  |  |  | Weather: Snow and freezing spray

## Slide 19
JAN 05, 06 UTC , 2016

## Slide 20
OVERLAND
STALLABRASS
SAWADA

## Slide 21: Jan 22, 2016
TIME UNKNOWN
22-Jan-16 |  |  | 41.86833 | -67.68 |  |  |  |  | weather was freezing spray, unobserved due to rough weather

## Slide 22
OVERLAND
STALLABRASS
SAWADA
X
Notes: This was close to maximum extent of Freezing spray for this event.

## Slide 23: Proposing a new approach (The most likely & the most threatening conditions)

## Slide 24: Proposing a new approach
PICK ME, PICK ME
OVERLAND
STALLABRASS
SAWADA
ATMOSPHERIC
ENVIRONMENT
INTENSITY
VESSEL
information
SPRAY
FLUX
PROBABILITY

## Slide 25: Proposing a new approach (The most likely & the most threatening conditions)
OVERLAND
STALLABRASS
SAWADA
X
March 08 2016- 18 UTC- 42HR Fcst

## Slide 26: Proposing a new approach
LGT
LGT
MDT
MDT
SVR
SVR
XTM
XTM
STALLABRASS
SAWADA
March 08 2016- 18 UTC- 42HR Fcst
90 HR Fcst

## Slide 27: Proposing a new approach
LGT
MDT
SVR
XTM
STALLABRASS
March 08 2016- 18 UTC- 42HR Fcst
MOST LIKELY
LIGHT
With LGT-MODT Prob.
MODERATE

## Slide 28: Proposing a new approach
LGT
MDT
SVR
XTM
SAWADA
March 08 2016- 18 UTC- 42HR Fcst
MOST LIKELY
LIGHT
MOST LIKELY.
MOD-SVR

## Slide 29: Proposing a new approach (The most likely & the most threatening conditions)
Most Likely
Most Dangerous
HIGH
Most Likely
Most Dangerous
MDT

## Slide 30: Where do we go from here ? (Need a EC-NOAA common objective)
    Overland, Stallabrass, Sawada ?
    Collaboration for next year ?
I am not sure that you will avoid the problem with this simplification. Freezing spray is dependent of water availability, and atmospheric conditions necessary to remove the heat from this water. The water availability will vary on different parts of one single ship, and it will be some variations between ships, but probably less variation for ships with the same bow shape. If one can assume a ship type with a bow shape like an MFV (medium-sized fishing vessel), and take into account icing only on a certain position of the ship (front of superstructure), it is possible to use a further modification of the Stallabrass algorithm to predict the icing rate and hence the onset of icing.
Icing prediction can then be referred to some standard vessel characteristics:
- medium-sized fishing vessel bow shape
- superstructure icing (average value at some height above deck level, for instance 3-5 m)
- vessel speed of 10 m/s
- direction always against the wind (wave direction might be different including swells) I have actually done this and created a model for the coast guard ship data I am using. To get a modification towards a larger ship, I use a lower spray frequency, and some additionally adjustments taken from observations from USGC Midgett. I also use a simplified trajectory model to calculate the droplet cooling time and speed of the droplets from an initial droplet and wind speed.
Icing rate categories are difficult, since there is variation in the literature regarding what should be reckoned as light, moderate or severe. (For instance uses Mertins (1968) ice accumulation in 24 hours, while Overland uses instantaneous icing rate converted to hourly rates)
From Eirik Samuelsen’ correspondances

## Slide 31: Where do we go from here ? (Need a EC-NOAA common objective)
Comments from Joseph Philllips: “Am I right in that you're proposing developing a probabilistic forecast between the three algorithms using a minimum spray flux specific to superstructure icing on a medium sized fishing vessels sailing against the wind at 10m/s? The probabilities would cover the light, moderate, severe, and extreme intensities? If so, I think this would probably be the best improvement to our service.”