## Slide 1: Finding Lift: Forecasting for Unpowered Flight
Tony Condon
Kansas Soaring Association
US Soaring Team

## Slide 3: Types of lift
Thermals
Ridge
Wave
Other interesting phenomenon
  Obstruction Wave
  Frontal Boundaries
  Outflow Boundaries
  Undular Bore

## Slide 6: Thermal Process
Sun Heats Ground
Ground Heats Air
“Trigger” and the bubble is released and rises
PV=nRT
Bubble cools at 3C (5.4F) / 1000 ft (Dry Adiabatic Lapse Rate)
Bubble continues to rise until it has cooled to equal the temperature of the surrounding air.

## Slide 8: Must have information:
Surface Temperature
  Forecasts generally pretty good
  Easy to take measurements
Temperature Aloft
  Direct measurement difficult
  Radiosondes in DDC & TOP not too helpful
  Computer models often miss forecast low inversions

## Slide 9
T.I.
Cloudbase

## Slide 11: Something Useful!
(Surface Temp – Dew Point)/2.2 = Cloudbase in 1000’s of ft

## Slide 12: What makes a good thermal soaring day
Relatively warm surface
Relatively cool air aloft
Cumulus Clouds
Light winds (Generally)

## Slide 14: NWS Hourly Forecast
Select “Mixing Height” under Fire Weather – AGL height of Thermals
Hourly Temp/Dew Point
Wind
Sky Cover

## Slide 16: Ridge Lift
Wind blowing up the side of a hill.
Minimum Wind Speed depends on shape of hill

## Slide 17: Mountain Wave
20 kts of Wind across the ridge line
Stable air at ridge top height
Increasing wind speed with altitude

## Slide 18: 20,000 ft over Oklahoma in Wave

## Slide 20: Obstruction Wave
Increasing Wind Speed with altitude
Wind blows up and over Cumulus

## Slide 21: Frontal Zone

## Slide 22: Outflow Boundary

## Slide 23: Undular Bore
“Compression Wave” upstream of a collapsing storm system
Morning Glory cloud
Well known in Australia
Observed but not explored in Kansas

## Slide 24: Questions??